## Slide 1: Smart home
By:
Taqi Eldeen Moanes
Ahmed Othman
Hosam Mohamed
John salama

## Slide 2: Introduction
Smart home that consists of GUI PC application and an embedded system based on ATmega32
User can monitor and control home devices including:
  Lights (Based on LDR)
  Fan (Based on LM35)
  Door status (servo motor)
  Electrical device (based on relay)

## Slide 3
User can enter home password that is saved on EEPROM
LCD for interactions with the user
Lockdown mode if password entered 3 times wrong
User can change the password using the GUI

## Slide 5: Embedded side, An overview
We used ATmega32 as the main controller for the system
HC-12 module for communication between PC and microcontroller
DC fan
LEDS for light simulation
Keypad for password entry
Internal EEPROM of ATmega32 is used for password saving
Buzzer for interaction with keypad and for alarm

## Slide 6: Embedded side, an overview
Relay is used to simulate an electrical device control
Servo motor is used to simulate door lock
LDR for light sensing
LM35 for temperature sensing

## Slide 9: Embedded side, Drivers
MCAL :
  ADC,
  TIM 0, 1, 2
  DIO
  EEPROM
  EXTI
  GIE
  UART

## Slide 10: Embedded side, Drivers
HAL :
  BUZZ
  DCM
  HC
  HOME_LIGHT
  KEYPAD
  LCD
  LDR
  SERVO
  TEMPS

## Slide 11: Embedded side, Application
Implementation of frames for communications between GUI and Microcontroller to monitor the status and control
Timeout for keypad 8 seconds if no activity
LCD display interactions such as greeting and after entering it display the temperature and light intensity
Buzzer sound when pressing a key
Buzzer alarm if 3 attempts is made incorrectly

## Slide 12: Embedded side, Application
Automatic light intensity control if enabled
Automatic fan control if enabled
TIM2 for servo control (on AND off)
TIM1 for PWM for fan
ADC for LM35 and LDR
UART for HC-12

## Slide 13: GUI side

## Slide 14: GUI side
User can interact with the system using the GUI
User Can turn ON/OFF the lights and enable/disable automatic control
User Can turn ON/OFF the Fan and enable/disable automatic control
User Can change the password of the lock
User Can use voice commands
Can control the electrical device
Can monitor the temperature of the inside and see the outside humidity and weather

## Slide 15: Thank you!